## Slide 1: University of Manchester
2023 Welding Centre

## Slide 2: What is Welding?
Welding is a high heat process which melts the base material. Typically, with the addition of a filler material.
Heat at a high temperature causes a pool of molten material which cools to form the join, which can be stronger than the parent metal. Pressure can also be used to produce a weld, either alongside the heat or by itself.
It can also use a shielding gas or granular flux to protect the molten weld pool and filler metals from becoming contaminated or oxidised. Welding is the most economical and efficient way to join metals permanently. It is the only way of joining two or more pieces of metal to make them act as a single piece. Welding is vital to our economy and ranks high among industrial processes and involves more sciences and variables than those involved in any other industrial process.

## Slide 3: Current welding facilities
Polysoude PC600. A water cooled 600amp automated column and boom Gas Tungsten Arc Weld (GTAW/TIG) system, inclusive of a 200mm deep narrow groove, containing a +/- 20mm oscillating electrode and wire feed head, with additional WP27 torch for thinner section welding and weld clad overlay capabilities.
1000kg capacity integrated manipulating table for circumferential welding applications.
70amp oscillating hot wire technology. The filler wire is pre-heated close to its melting point before it is fed into the arc weld pool. Vastly increasing deposition rates.

## Slide 4: Current welding facilities
High deposition water cooled 2400amp Submerged Arc Weld (SAW) automated column and boom welding system. With tandem, narrow groove, single and twin wire feeds.
Miller strip cladding head with a capacity to deposit single weld bead widths varying from 25mm to 70mm in both Electroslag Strip Welding (ESW) and SAW for high deposition cladding applications.
MSD -The magnetic steering device is intended for use with the ESW process it ensures that the cladding process achieves uniformity, in terms of a level and uniform weld bead edge formation. Additionally, it controls the weld bead ripple formation which maintains the consistency of both bond integrity and appearance.

## Slide 5: Current Welding facilities
3 x Miller Dynasty 350, Manual- Gas Tungsten Arc Welding machines (GTAW/TIG) with AC/DC capabilities.
The Miller Dynasty 350 offers the very latest technology in the science of TIG welding. Very powerful and compact, this 350 amp pulsed AC/DC water cooled Miller TIG welder delivers superior arc performance with total AC arc-shaping capabilities.
Miller Dynasty 350, Manual- Shielded Metal Arc Welding (SMAW/MMA)with AC/DC capabilities.
Huntingdon Fusion Technologies flexible inert gas welding enclosure

## Slide 6: TIG welding facilities

## Slide 7: Current Welding facilities
The Miller Auto Axcess 450 is a manual and automated robotic arc welding power supply system. It is designed for automating Gas Metal Arc Welding (GMAW/MIG) and flux cored applications. The AA 450 DI features multiple MIG welding programs including Accu-Pulse, Accu-Curve, standard or adaptive pulse, conventional MIG, and metal core programs. The Accu-Pulse setting is especially advantageous as it provides precise arc control for tight corners or tack welds, ensuring quality.
The Miller Auto Axcess 450 is suitable for the welding/brazing of most grades of aluminium, steel, stainless steel.

## Slide 8: MIG welding facilities

## Slide 9: Current Welding facilities
Welding restraint/clamping fixture for the butt welding of up to 200mm thick weldments with run on and run off capabilities. Fully adjustable in length for longer samples, combined with individual adjustable feet to align the weldments to within +/-0.5mm.The restraining forces that are applied to the weld test pieces can be documented by recording the pressure of the hydraulic oil, and noting the cross-sectional area of the rams. The oil pressure is then recorded for each pass. Strain gauges are also attached to the king plates on the restraint rig, so that the bending moments in the king plates can be recovered.

## Slide 10: Current Welding facilities
Meta Vision camera system, for live arc on recording.
The welding camera is used for the monitoring of all open arc welding processes with user interchangeable lens capability and digital output. The high resolution ensures concise images to the smallest detail allowing for easy quality control.

## Slide 11: Current Welding facilities
70kVA, 6 channel, S/S, Heat Treatment Module with Advantage3 temperature programmer/controllers. Stork Cooperheat’s 70kVA Heat Treatment Modules include the unique ‘Advantage 3’ temperature programmer/controllers which ensure the required temperature uniformity within each control zone.
The goal of preheating and post weld (PWHT) heating is to maintain temperature between weld passes and to uniformly control changes in target temperatures. By properly achieving, maintaining, and then cooling weld temperatures, you lower weld stress, distortion, reduce shrinkage stress and allow unwanted hydrogen to escape.

## Slide 12: Current Welding facilities
The highly flexible and durable KUKA KR 30 handles diverse applications. Its modular design allows for simple payload and reach modifications. With a small footprint and variable mounting options, the KR 30 fits the bill for space-efficiency and versatility. The KR 30 robot is easily customized for different projects and requirements. It is capable of low to medium payloads, with powerful and accurate movements. The KR30 has curently been adapted to suit a range of GMAW(MIG) processes with the addition of the IPG 16KW fibre laser welding system complete with wire delivery systems.

## Slide 13: Current welding facilities
Sunstone PA250i Micro TIG Welder
Dissimilar Welding Capabilities. The 250i’s power capabilities let you weld many dissimilar metal combinations!
Weld materials as Thin as 0.0005” (0.0127mm). Enjoys extreme flexibility with its TIG head, resistance wheel and spot welding capabilities.

## Slide 14: Guillotine, rolling and bending facilities

## Slide 15: Oval Q 230v - Plastic Fabrication Hot Air Welding Kit
For professional plastic welding of plastic fabrication products such as: Chemical Tanks, PVC & PP Ventilation or Ductwork Fittings and Pipe, Plastic Fume Cupboards.

## Slide 16: GULLCO WELDING POSITIONER GPP-250-M
Gullco's Welding Positioner is a positive drive rotary turn table complete with mounting flange and chuck with drive and tilt mechanism with microprocessor based pulse width modulation motor control. Purge-Equipped for internal back purging for all manual TIG and MIG welding applications.

## Slide 17: Current Welding facilities
With a SWL 1000kg capacity lift, the floor crane provides a Hydraulic powered lift with electric drive motors for effortless propulsion of goods and equipment making for an extremely maneuverable version of what would otherwise be a very heavy and awkward lift. Pivoting Arm Counterbalance floor crane has a 30 degree pivoting arm, making hard to reach lifts accessible

## Slide 18: Current Welding Facilities
Down draft table with cartridge filters. The down draft table mod. POLIJET is a self contained unit featuring sophisticated cartridge filters (instead of common filter bags), which are capable of filtering particle sizes down to 0,2÷2 microns, filtering efficiency is rated at 99,9%. Cleaning of the cartridges is done by a jet of compressed air, via a pneumatic switch. The engineering study and design of every aspect of this unit, including the slot openings, guarantees that all fumes and harmful dust are immediately captured at the source, thus eliminating a health hazard.

## Slide 19: Current Welding Facilities
Hypertherm 85 Manual plasma cutting process, produces a DC current that flows through this connection, and initiates the plasma gas flow. Once the plasma gas (compressed air) builds up enough pressure, the electrode and nozzle are forced apart, which causes an electrical spark that converts the air into a plasma jet. The DC current flow then switches from electrode to nozzle, to a path between the electrode and work piece. Capable of cutting thicknesses up to 20mm thick.

## Slide 20: 5 Ton overhead crane capacity