## Slide 1: Project Presentation: How to green your cell culture
Student: Ornella Trombetta
Supervisor: Forbes Mason
X: @FBMH_SR
#ESShowcase24

## Slide 2: Introduction
#ESShowcase24
What is cell passaging?
Cell passaging is the basic and most routine SOP in cell culture to maintain cell lines, therefore it is the best place to start looking at green SOP
Aim: To improve sustainability of cell culture by allowing laboratories to pick and choose green SOPs to implement in their laboratories for cell lines in BSL1 and BSL2
Green SOP will involve:
Reducing plastic use
Reducing FBS use
Notes: 1 minute
Interacting with audience: who uses/directs cell culture laboratories?
Starting from passaging cells, it is the maintenance of cell lines. For adherent cells, once they cover around 70-80% of their plate they must be removed and reseeded. This involves the use of PBS to wash away residual old media, trypsin enzymes to detach them from their dish or flask, re-diluting the cells and aliquoting them in new dishes or flasks, and finally topping it up with additional new media.
So this is the fundamental step for the maintenance of cells and all of the steps involve plasticware to transfer reagents, and handle cells in different vessels
Therefore we aim to improve the sustainability of cell culture by providing scientists with greener SOP to design their own greener cell culture.
Here, I have explored ways to reduce plastic usage in cell culture, as well as addressing the potential to reduce the consumption of Foetal Bovine serum to feed cells nutrients. This is because FBS has been associated with many ethical issues which pose a threat to animal well-being, as well as issues with availability, scandals, and inconsistency with nutrient concentrations across different bottles
We will explore these concepts while keeping in mind of the balance between strategies to reduce environmental impact, and the quality of the science and quality of the cell lines

## Slide 3: Reusing plastic
#ESShowcase24
HEK293T cells were seeded in 10% FBS and 1% antibiotics
Also tested without antibiotics up to 5 passages
Culture vessels
Evidence
Vessel | Total CO2 equivalent for 1 piece
10 cm diameter Petri dish | 96 gCO2 or 0.6 km
T75 (75 cm2 surface) flask | 251 gCO2 or 1.4 km
174 gCO2 = 1 km by car
Notes: 30 seconds
Through various evidences and calculations, we can assume that 174 gCO2 is equivalent to traveling around 1 kilometre by car. I will use this to illustrate the impact of plastic.
So for example, cells are typically cultured in either Petri dishes or flasks which have a variable environmental impact between 0.6-1.5 km for each piece. These numbers include both the production of the product, and the decontamination steps after use.
Here, I will show you how instead of transferring cells to a new plate, the old plate can actually just be washed with PBS and the same cells as before can be reseeded in their old vessel
HEK293T cells grown in normal media with antibiotic showed no difference compared to cells grown on a dish that was reused for the third time
In addition, dishes were also reused 5 times without antibiotics and no differences could be seen
/////

## Slide 4: Reusing plastic
#ESShowcase24
1 person doing 3 cell passages per week for 45 work weeks of one cell line with a 18-36 h duplication rate consumes vessels
Reusing the vessels 5 times saves the equivalent of 108 vessels, 60-155 km, and £90-300 with no difference in quality of the cell culture
Vessel | Total CO2 equivalent for 1 piece | Yearly consumption (135 pieces / person) | Yearly consumption reusing dishes 5 times (27 pieces) / person
10 cm dish | 96 gCO2 or 0.6 km | 13 000 gCO2 or 75 km | 2600 gCO2 or 15 km
T75 flask | 251 gCO2 or 1.4 km | 34 000 gCO2 or 195 km | 6800 gCO2 or 40 km
Culture vessels
Impact simulation
Notes: 30 seconds
/////
So, what positive impact does this actually have?
If we imagine one person passaging a single cell line 3 times a week for 45 weeks, they would use 135 dishes/flasks in total and produce the equivalent of 75-195 km worth of CO2
Instead if we reuse these vessels 5 times, we will save the equivalent of 60-155 km, and up to £300 per person per cell line per year

## Slide 5: Reusing plastic
#ESShowcase24
Evidence
HEK293T 10% FBS but no antibiotics
Images were taken at the 5th passage of reusing pipettes for PBS, Trypsin, and media
Tool | Total CO2 equivalent
5 ml serological pipette | 34 gCO2 or 0.2 km
Reusing volume measuring tools
Reuse serological and Pasteur pipettes for the same solution, in the same working session
New plastic Reused plastic
Notes: 30 seconds
Cell culture also requires a lot of serological pipettes to measure trypsin, PBS, media, cell aliquots. So a typical 5 ml pipette will produce around 200 m worth of CO2.
In order to reduce pipette usage, we tested the potential for cell contamination if we were to reuse the same pipette for the same solution, such as a pipette for PBS or Trypsin, within one work session in the biosafety cabinet. Importantly the pipette is placed back into its original packaging after every use, and of course it must not touch the cells
In HEK293 grown without antibiotics while reusing pipettes for PBS, Trypsin, and media there was no visible change in cell growth or mortality
/////////

## Slide 6: Reusing plastic
#ESShowcase24
Reusing volume measuring tools
1 person using the safety cabinet may consume 10 5 ml serological pipettes for a single reagent.
Using the cabinet 3 times/week for 45 work weeks consumes pipettes in total
Reusing the vessels 5 times saves the equivalent of 1215 pipettes, 238 km, and £343
with no difference in quality of the cell culture
Impact simulation
Tool | Total CO2 equivalent | Yearly consumption (1350 pieces / reagent / person) | Yearly consumption reusing the tool in one session
5 ml serological pipette | 34 gCO2 or 0.2 km | 46 000 or 264 km | 4600 or 26 km
Reuse serological and Pasteur pipettes for the same solution, in the same working session
Notes: 30 seconds
/////////
So again what impact would this have in our laboratories?
Say one person that consumes 10 serological pipets for one reagent in the biosafety cabinet, three times a week, for 45 weeks, this is equal to 1350 pipettes in total for one reagent, or 264 km worth of CO2
If instead we reuse the pipette during one work session, we can save 1215 pipettes, 238 km worth of CO2, and also £340 pounds worth of pipettes

## Slide 7: Reducing plastic
#ESShowcase24
  Using 135 T25 flasks instead of T75 flasks saves 20700 gCO2 or 120 km equivalent
  Using 135 6 cm dishes instead of T25 flasks saves 8500 gCO2 or 115 km equivalent
  Saving 135 tubes saves 3501 gCO2 or 20 km
  Use TrypLE for loosely adherent cell lines
  Using 135 1ml Pasteur pipettes for Trypsin and 135 for cell aliquoting (270 total) instead of 5 ml serological pipettes saves 3560 gCO2 or 21 km
Notes: 1 minute
Other sustainability ideas to consider using is to consciously reduce the physical weight of the tools you use.
For example if we use smaller volume cell vessels such as flasks, we can save as much as 120 km worth of CO2 if we use T25 instead of T75 flasks
Another example is to consider using Petri dishes instead of T25 flasks, which would save 115 km work of CO2 per year per cell line
As for serological pipettes, choosing appropriately small options such as Pasteur pipets would save around 21 km equivalent
If instead we skip the centrifuge step altogether or use TrypLE gentle enzymes for more loosely adherent cell lines, we can also save another 20 km equivalent per person per cell line

## Slide 8: Reducing FBS to 5%
#ESShowcase24
HEK293T was also tested and obtained the same results
Ethics:
Reducing the quantity of animals needed per year by half
Cost:
ThermoFisher basic HI-FBS is £270 / 500 ml
10% FBS in 500 ml media is £27
5% FBS in 500 ml media is £13.5
With no difference in quality of the cell culture
Evidence
Impact
Why not try out lower FBS concentrations with your cell lines of interest?
RPE1 cells
Notes: 1 minute
As for reducing the consumption of FBS, we can begin trialling reduced concentrations for our established cell lines.
For example, for RPE1 cells there was no visible difference in cell growth or death numbers within a 48 h incubation period. This was the same in HEK293T cells.
This has significant impacts for the demand of FBS, therefore decreasing its demand of animals and costs by half without affecting the quality of the cells

## Slide 9: Replacing FBS
#ESShowcase24
Adult Bovine Serum (ABS)
Similar results shown in other cells lines:
  Loosely adherent (HEK293T, BV-2, Neuro2A),
  Strongly adherent (Panc1)
  Suspension (THP1)
Ethics
Will save approximately 48-176 calves
Costs
ThermoFisher basic FBS is £270 / 500 ml
ThermoFisher ABS £89/ 500 ml
Saving £181 per 500 ml bottle
With no difference in quality of the cell culture
Impact
Why not try samples of FBS alternatives such as ABS with your cell lines of interest?
Evidence
RPE1 cells
Notes: 1 minute
Due to availability, ethics, and scientific concerns regarding FBS, we must begin to consider alternatives
For example, if we consider adult bovine sera instead of serum we can produce the equivalent sera volume of 48-176 bovine foetuses with just one cow from the meat industry.
The adult serum was tested on a variety of cells. For example, strongly adherent RPE1 cells acclimatised to ABS for 5 passages and then tested during a 48 h period showed no differences in cell morphology or proliferation number.
With the help of volunteers, other cell lines were tested and in total a variety of loosely adherent, strongly adherent, and suspension cell lines also showed similar results.
So the impact of this, of course, would be to completely remove the need for all bovine foetuses, and for adult bovine sera in particular this would reduce the cost of growth supplements by £180 per 500 ml at minimum.

## Slide 10: Conclusions
#ESShowcase24
Limitations and future perspectives
Long-term cell culture of each green SOP
Contamination tests such as MycoStrip to directly quantify differences between new and reused plastic which may affect aseptic technique
Transcriptomic and proteomic changes in cells in different or reduced supplements
What is your next step?
Notes: 1 minute
So to conclude, there is still a lot of work to be done in this area of environmental sustainability, and really the three most important next steps would be to get an understanding of any long term implications of any green SOP, in addition to quantify any potential changes in contamination when reusing plastic, as well as transcriptomic and proteomics data from across different cell lines when reducing or replacing FBS which future research or manufacturers may provide.
Nevertheless, this research provides with evidence that cell culture sustainability can be significantly improved, and these green methods and ideas can already begin to be undertaken in laboratories. Therefore now it is up to you to decide which are the best designs for your laboratories.

## Slide 11
FBS is not the best
FBS manufacturers have shown inconsistencies with ethical standards, availability, contamination, and adulteration of batches. It is time to start thinking of a future without FBS.
Reduce FBS consumption
Reducing FBS from 10% to 5% may be a viable option for your cell line. This was tested with HEK293 and RPE1. Why not give it a try?
Green your cell culture
SUSTAINABLE
LEAF AND 6R:
MAKING SCIENCE
Choose better consumables
Switch to Pasteur or small volume serological pipets (1-2 mL) for Trypsin and Cryogenic fluid instead of 5 mL serological pipets.
Have an aspirator? Use dishes instead of flasks with the same surface area.
Choose better practices
Strongly adherent cell lines don’t need a centrifuge step and weak cell lines can use gentle TrypLE. Skip the centrifuge tube!
Waste
Ethics
Explore
Protocols
Reusing culture dishes and flasks (left) in consecutive passages of one cell line up does not pose risk of contamination, and saves money. Detach your cells properly, wash with PBS 2x, and seed the cells back in!
Similarly, you can place serological and Pasteur pipets in their original packaging and reuse them for the same reagent in the same working session. Then discard them!
RPE1 cells cultured in FBS or ABS (right). Scale bar, 100 μm.
Explore alternatives to FBS
Other bovine sera such as Adult bovine sera (ABS) have shown comparable performance to FBS. Why not try it for ¼ the price of FBS?
Watchout for literature validating other cost-effective alternatives such as GroPro human platelet lysate solution and Chemically Defined Lipid Concentrate!
Explore

## Slide 12: Appendix
#ESShowcase24
BSL2 cell lines
  Human-derived cell lines (because they can carry human diseases)
  Any genetically engineered cell lines with potentially hazardous modifications
  Any genetically engineered cell lines via virus transfection
  Any artificially immortalised cell lines e.g. RPE1 human retinal pigment epithelial
BSL1 cell lines
  Non-human
  Well-characterized, non-artificially immortalised cell lines, e.g. Neuro2A mouse neuroblastoma
What are BSL1 and BSL2?

## Slide 13: Appendix
#ESShowcase24
Impact calculations
For example, 1 g of polystyrene (PS) was identified as 3.80 gCO2eq (C product), in addition cell culture waste decontamination was identified as 0.34 gCO2eq to autoclave 1 g of any plastic, along with incineration with energy recovery identified as 1.07 gCO2eq/g for PS. This makes a total of 5.21 gCO2eq per 1 g of PS.

## Slide 14: Appendix
#ESShowcase24
Reusing dishes AND avoiding use of falcon tubes
This method is particularly used in suspended cell cultures already

## Slide 15: Appendix
#ESShowcase24
Cell lines used
Loose (easily detached)
  HEK293T, human embryo kidney, BSL2
  BV2, immortalized mouse microglial cell line, BSL1-2
  Neuro2A, mouse neuroblastoma, BSL1
Strong (need longer Trypsin treat and shaking to detach them)
  RPE1, immortalised human retinal pigment epithelial cell line, BSL2
  Panc1, human pancreatic cancer cell line, BSL2
Suspension
  THP1, human monocytic cell line derived from acute monocytic leukemia, BSL2
Acknowledgements: F. Clifton-Spring; D. Ho; H. Meng; and R. McDowell and S. Notash for providing additional insight on FBS alternatives in the cell lines highlighted in bold above

## Slide 16: Appendix
#ESShowcase24
Gestation of 3-9 months (calf gestation is ~9 months
Poor documentation of standard procedures across stockyards/abattoirs, and across countries
The slaughter is often ‘accidental’
  With development of pregnancy diagnosis technology, and th need for correct vet checks for the cows, it is now more difficult to acquire FBS
  Feeds into the occasionally scarcity of FBS
FBS components concentrations are highly variable frm bottle to bottle
  Reproducibility and reliability of data
Incorporation of FBS components in cells (antibodies and receptors etc) which may change cell behaviour
  Feeds into the use of FBS-cultured cells for production of pharmaceutical products
Scandals across decades regarding the presence of prions and other pathogenic agents, and adulteration of batches
Issues of Foetal Bovine Serum

## Slide 17: Appendix
#ESShowcase24
Sera volumes
Foetal bovine sera production (data from ThermoFisher)
  3 month gestation make ~150 ml
  9 month gestation (almost to term) ~550 ml
Adult bovine sera production estimation
  Adult cow of 600kg
  Assuming 8% of body weight in blood = 48 kg
  Assuming sera is 55% of the blood = 26.4 litres of adult bovine sera / 600 kg